## Slide 1: Autonomous Navigation for Flying Robots Lecture 2.3: 2D Robot Example
Jürgen Sturm
Technische Universität München

## Slide 2: 2D Robot
Robot is located somewhere in space

## Slide 3: 2D Robot
Robot is located somewhere in space
Robot pose:
  Position
  Orientation (yaw angle/heading)

## Slide 4: Robot Pose
Robot is located somewhere in space
Robot pose:
  Position
  Orientation (yaw angle/heading)
Robot pose represented as transformation matrix:

## Slide 5: Robot Pose
Robot is located at
Robot pose

## Slide 6: Coordinate Transformations
Robot is located somewhere in space
Robot pose:
  Position
  Orientation (yaw angle/heading)
What is the pose after moving 1m forward?
How do we need to move to reach a certain position?

## Slide 7: Coordinate Transformations
Robot moves forward by 1m
What is its position afterwards?
Point located 1m in front of the robot in local coordinates:

## Slide 8: Coordinate Transformations
Robot moves forward by 1m
What is its position afterwards?
Point located 1m in front of the robot in global coordinates:

## Slide 9: Coordinate Transformations
We transformed local to global coordinates
Sometimes we need to do the inverse
How can we transform global coordinates into local coordinates?

## Slide 10: Coordinate Transformations
We transformed local to global coordinates
Sometimes we need to do the inverse
How can we transform global coordinates into local coordinates?

## Slide 11: Coordinate Transformations
Now consider a different motion
Robot moves 0.2m forward, 0.1m sideward and turns by 10deg
Euclidean transformation:

## Slide 12: Coordinate System Transformations
Now consider a different motion
Robot moves 0.2m forward, 0.1m sideward and turns by 10deg
After this motion, the robot pose becomes

## Slide 13: Coordinate System Transformations
Note: The order matters!
Compare:
Move 1m forward, then turn 90deg left
Turn 90deg left, then move 1m forward
1.
2.

## Slide 14: Robot Odometry
How can we estimate the robot motion?
Control-based models predict the estimated motion from the issued control commands
Odometry-based models are used when systems are equipped with distance sensors (e.g., wheel encoders)
Velocity-based models have to be applied when no wheel encoders are given

## Slide 15: Dead Reckoning
Integration of odometry is also called dead reckoning
Mathematical procedure to determine the present location of a vehicle
Achieved by calculating the current pose of the vehicle based on the estimated/measured velocities and the elapsed time

## Slide 16: Motion Models
Estimating the robot pose based on the issued controls (or IMU readings) and the previous location
Motion model

## Slide 17: Exercise
Given:
  IMU readings from real flight of Ardrone quadrotor
  Horizontal speed in the local frame
  Yaw angular speed
  Wanted:
    Position and orientation in global frame
  Integrate these values to get robot pose

## Slide 18: Lessons Learned
2D pose
Conversion between local and global coordinates
Concatenation of (robot) motions
Robot odometry