## Slide 1: Autonomous Navigation for Flying Robots Lecture 7.1: 2D Motion Estimation in Images
Jürgen Sturm
Technische Universität München

## Slide 2: 3D to 2D Perspective Projections
Richard Szeliski, Computer Vision: Algorithms and Applications
http://szeliski.org/Book/

## Slide 3: 3D to 2D Perspective Projections
Richard Szeliski, Computer Vision: Algorithms and Applications
http://szeliski.org/Book/

## Slide 4: Images
We can think of an image as a function
gives the intensity at position
Realistically, the image function is only defined on a rectangle and has finite range

## Slide 5: Digital Images
Image function is sampled discrete pixel locations
Image can be represented as a matrix
111 | 115 | 113 | 111 | 112 | 111 | 112 | 111
135 | 138 | 137 | 139 | 145 | 146 | 149 | 147
163 | 168 | 188 | 196 | 206 | 202 | 206 | 207
180 | 184 | 206 | 219 | 202 | 200 | 195 | 193
189 | 193 | 214 | 216 | 104 | 79 | 83 | 77
191 | 201 | 217 | 220 | 103 | 59 | 60 | 68
195 | 205 | 216 | 222 | 113 | 68 | 69 | 83
199 | 203 | 223 | 228 | 108 | 68 | 71 | 77

## Slide 6: Problem Statement
Given: two camera images
Goal: estimate the camera motion
For the moment, let’s assume that the camera only moves in the xy-plane, i.e.,
Extension to 3D follows

## Slide 7: General Idea
Define an error metric that defines how well the two images match given a motion vector
Find the motion vector with the lowest error

## Slide 8: Error Metrics for Image Comparison
Sum of Squared Differences (SSD) with displacement and residual errors

## Slide 9: Windowed SSD
Images (and image patches) have finite size
Standard SSD has a bias towards smaller overlaps (less error terms)
Solution: divide by the overlap area
Root mean square error

## Slide 10: Cross Correlation
Maximize the product (instead of minimizing the differences)
Normalized cross correlation (between -1..1)
Less sensitive to illumination changes

## Slide 11: General Idea
Define an error metric that defines how well the two images match given a motion vector
Find the motion vector with the lowest error

## Slide 12: Finding the minimum
Full search (e.g., ±16 pixels)
Gradient descent
Hierarchical motion estimation

## Slide 13: Motion Estimation
Perform Gauss-Newton minimization on the SSD energy function (Lucas and Kanade, 1981)
Gauss-Newton minimization
  Linearize residuals w.r.t. to camera motion
  Yields quadratic cost function
  Build normal equations and solve linear system

## Slide 14: Motion Estimation
Error function
Linearize in u

## Slide 15: Motion Estimation
Taylor expansion of energy function with

## Slide 16: Least Squares Minimization
Goal: Minimize
Solution: Compute derivative and set to zero with and

## Slide 17: Least Squares Minimization
Step 1: Compute A,b from image gradients using with and

## Slide 18: Least Squares Minimization
Step 2: Solve linear system
Note: All of the required computations are super-fast!
In step 1: image gradients + summation to build A,b
In step 2: solve a 2x2 linear equation

## Slide 19: Hierarchical Motion Estimation
Construct image pyramid by downsampling
Estimate motion on coarse level
Use as initialization for next finer level

## Slide 20: Covariance of the Estimated Motion
Assuming (small) Gaussian noise in the images with
… results in uncertainty in the motion estimate with covariance (e.g., useful for Kalman filter)

## Slide 21: Optical Computer Mouse (since 1999)
E.g., ADNS3080 from Agilent Technologies, 2005
  6400 fps
  30x30 pixels
  4 USD
http://www.alldatasheet.com/datasheet-pdf/pdf/203607/AVAGO/ADNS-3080.html

## Slide 22: Image Patches
Sometimes we are interested of the motion of small image patches
Problem: some patches are easier to track than others
Which patches are easy/difficult to track?
How can we recognize “good” patches?

## Slide 23: Image Patches
Sometimes we are interested of the motion of a small image patches
Problem: some patches are easier to track than others

## Slide 24: Example
Let’s look at the shape of the energy
Richard Szeliski, Computer Vision: Algorithms and Applications
http://szeliski.org/Book/

## Slide 25: Corner Detection
Idea: Inspect eigenvalues of matrix A (Hessian)
  small  no point of interest
  large, small  edge
  large  corner

## Slide 26: Corner Detection
Harris detector (does not need eigenvalues)
Shi-Tomasi (or Kanade-Lucas)

## Slide 27: Other Detectors
Förstner detector: localize corner with sub-pixel accuracy
FAST corners: learn decision tree, minimize number of tests  super fast
Difference of Gaussians (DoG): scale-invariant detector used for SIFT
…

## Slide 28: Kanade-Lucas-Tomasi (KLT) Tracker
Algorithm
  Find (Shi-Tomasi) corners in first frame and initialize tracks
  Track from frame to frame
  Delete track if error exceeds threshold
  Initialize additional tracks when necessary
  Repeat step 2-4

## Slide 29: KLT Tracker
KLT tracker is highly efficient (real-time on CPU) but provides only sparse motion vectors
Dense optical flow methods require GPU

## Slide 30: Demo of a KLT Tracker
Visual Servoing Platform (ViSP), 2010. http://www.irisa.fr/lagadic/visp/visp.html
https://www.youtube.com/watch?v=a0B2nBj4FAM

## Slide 31: Lessons Learned
2D motion estimation
Cost functions
Optical computer mouse
Corner detectors
KLT Tracker
Next: Visual odometry